## Slide 1: Digital Image Processing Technologies & Applications
Representation & Description

## Slide 2: Contents
This lecture will cover:
  Overview
  Representation
  Boundary descriptor

## Slide 3: Overview
After an image has been segmented into regions. Representation and description should be considered.
Representation and description used to make the data useful to a computer.
Representing region in 2 ways:
  In terms of its external characteristics (its boundary)  focus on shape characteristics.
  In terms of its internal characteristics (its region)  focus on regional properties, e.g., color, texture.
Sometimes, we may need to use both ways.

## Slide 4: Overview
Choosing a representation scheme, however is only the part of the task of making data useful to computer.
The next task is to describe the region based on the chosen representation.
For example:
  Representation  boundary.
  Description  length of the boundary, orientation of the straight line joining its extreme points, and the number of concavities in the boundary.

## Slide 5: Sensitivity
Feature selected as descriptors should be as insensitive as possible to variations in
  size
  translation
  rotation
Following descriptors satisfy one or more of these properties.

## Slide 6: Representation
Segmentation techniques yield raw data in the form of pixels along a boundary or pixels contained in a region.
These data sometimes are used directly to obtain descriptors.
Standard uses techniques to compute more useful data (descriptors) from the raw data in order to decrease the size of data.

## Slide 7: Chain Codes
4 Directional chain code:
0321
8 Directional chain code:
07654321

## Slide 8: Chain Codes
Unacceptable because
  The resulting chain codes tends to be quite long.
  Any small disturbances along the boundary due to noise or imperfect segmentation cause changes in the code that may not be related to the shape of the boundary.

## Slide 9: Chain Codes
Circumvent the problems by
  Resample the boundary by selecting a larger grid spacing.
  Then, as the boundary is traversed, a boundary point is assigned to each node of the large grid, depending on the proximity of the original boundary to that node.

## Slide 10: Chain Codes
0033333323221211101101
076666553321212
However, different grid can generate different chain codes.
The accuracy of the resulting code representation depends on the spacing of the sampling grid.

## Slide 11: Normalized Chain Codes
0
1
2
2
3
3
0
1
0
1
2
2
3
3
0
1
3 3 2 2 1 0 1 0
1 0 1 0 3 3 2 2
0 1 0 3 3 2 2 1
The chain code of a boundary is depend on the starting point.
However, the code can be normalized with respect to the starting point by a straightforward procedure.
We simply treat the chain code as a circular sequence of direction numbers and redefine the starting point so that the resulting sequence of numbers form an integer of minimum magnitude.

## Slide 12: Normalized Chain Codes
Rotate 90 degree
0
1
2
2
3
3
0
1
0
0
2
1
3
3
1
2
(2)
1
0
1
0
3
3
2
2
3
3
1
3
3
0
3
0
(3)
2
1
2
1
0
0
3
3
3
3
1
3
3
0
3
0
The chain code can be also normalized by using the first difference of the chain code. Then it is insensitive to rotation.
Size normalization can be achieved by altering the size of the re-sampling grid.
If original chain code is: MN=a0a1…an-1, N=4 or 8
And The first difference chain code is: M’N=b0b1…bn-1
Then b0=(a0-an-1) MOD N, bi=(ai-ai-1) MOD N

## Slide 13: Normalized Chain Codes

## Slide 14: Chain Code Smoothing
Chain code smoothing template:
Broken arrowhead：Original 8- Directional chain code between pixels p and q
Real line arrowhead: The smoothed chain code.
N8 | N8 | N8
N8 | P | N8
N8 | N8 | N8

## Slide 15: Chain Code Smoothing
Chain code smoothing example:

## Slide 16: Chain Code Smoothing
SCC Chain code (斜率链码):

## Slide 17: Polygonal Approximations
Boundary can be approximated with arbitrary accuracy by a polygon.
For a closed curve, the approximation is exact when the number of the segments in the polygon is equal to the number of points in the boundary.
The goal: Try to capture the “essence” of the boundary shape with the fewest possible polygonal segments.
Not trivial and time consuming.
Three methods:
  Minimum perimeter polygons
  Merging techniques
  Splitting techniques
Notes: perimeter
n. 周长；周界；[眼科] 视野计

## Slide 18: Minimum Perimeter Polygons

## Slide 19: Minimum Perimeter Polygons

## Slide 20: Minimum Perimeter Polygons

## Slide 21: Merging Techniques
Merge points along the boundary, until the distance exceeds a preset threshold.
The procedure is repeated, merging new points along the boundary until the distance again exceeds the threshold.
Points: 15, edges: 14
Points: 5, edges: 4

## Slide 22: Merging Techniques
a
b
c
d
e
f
g
h
i
j
k
1
2
3
An Example:
Problem: the vertices in the resulting approximation do not always correspond to inflections (such as corners) in the original boundary.
Notes: inflection
n. 弯曲，变形；音调变化

## Slide 23: Splitting techniques
Find the major axis.
Find max axes which perpendicular to major axis and has distance greater than a threshold.
Repeat until we can’t split anymore.
Splitting technique is to subdivide a segment successive into two parts until a specified criterion is satisfied.

## Slide 24: Splitting techniques
a
b
c
d
e
f
g
h
i
j
k
a
b
c
d
e
f
g
h
i
j
k
Different thresholds lead to different results.

## Slide 25: Landmark Points
Landmark Points (地标点或标志点)
Notes: 地标点是一种近似表达方法，但当将边界转换为地标点后经常不能将其恢复回去。所用的地标点数目不同，近似的程度也不同。一般来说，地标点越多，近似的程度越好。地标点的选择也很重要。

## Slide 26: Landmark Points
Method | Expression | Note
2n-vector | So = [1, 1, 1, 2, 2, 1] | So是一个2n×1的实坐标矢量
2n-set | Sf = {1, 1, 1, 2, 2, 1} | Sf 是一个包含2n个实坐标的集合
Matrix |  | Sv 是一个n×2 的矩阵，每行包含一个标志点的x-和y-实坐标
Plural-plane |  | Sc是一个n× 1 的复数矢量，每个复数表示一个标志点的x-和y-坐标
Landmark points expression:
S1 = (1, 1)，S2 = (1, 2)，S3 = (2, 1)

## Slide 27: Signatures
Map 2D function to 1D function.
One of the simplest way is to plot the distance from the centroid to the boundary as a function of angle.

## Slide 28: Signatures
Signatures are invariant to translation.
Normalization with respect to rotation can be achieved by finding a way to select the same starting point.
One way to do so is to select the starting point as the point farthest from the centroid, if the point happens to be unique and independent of rotational for each shape of interest.

## Slide 29: Signatures
y – s curve（切线角为弧长的函数）
From each point along the object boundary, make a tangent, y is tangent angle respecting to the reference x axis. s is the length of the arc.

## Slide 30: Signatures

## Slide 31: Boundary Segments
Decomposing a boundary into segments often is useful.
Decomposition reduces the boundary’s complexity and thus simplifies the description process.
Convex hull is a powerful tool for robust decomposition of the boundary.
Convex hull H of an arbitrary set S is the smallest convex set containing S.

## Slide 32: Boundary Segments
The set different H-S is called convex deficiency D (凸形缺陷) of the set S.
D
H=S+D

## Slide 33: Boundary Segments
The region boundary can be partitioned by following the contour of S and marking the points at which a transition is made into or out of a component of the convex deficiency.
In practice, digital boundaries tend to be irregular because of digitization, noise. These effect usually result in convex deficiency:
  To smooth a boundary prior to partitioning.
  Use a polygonal approximation first.

## Slide 34: Skeletons
We already discussed the basics of skeleton using morphology. However, as noted in that section, the procedure made no provision for keeping the skeleton connected.
The algorithm developed here corrects that problem.

## Slide 35: Skeletons
B
R

## Slide 36: Skeletons
The same results would be obtained with the maximum disk of section 9.5.7

## Slide 37: Skeletons
Although the MAT of a region yields an intuitively pleasing skeleton, directly implementation of this definition is expensive computationally.
Numerous algorithms have been proposed for improving computational efficiency.
Typically, these are thinning algorithm that iteratively delete edge points of a region subject to the constraints that deletion of these points:
  1)Does not remove end points.
  2)Does not break connectivity.
  3)Does not cause excessive erosion of the region.
Notes: excessive
adj. 过度的，过多的

## Slide 38: Skeletons
Assume region points have value 1 and background points have value 0.
Here we will introduce a method that consists two steps applied to the contour points of the given region.
Contour points, as define in Section 2.5.2, are any pixels with value 1, and having at least one 8-neighborhood value 0.

## Slide 39: Skeletons
Thinning Algorithm:
With reference to the 8-neighborhood notations shown in Fig. 13.8, step 1 flags a contour point for deletion, if the following conditions are satisfied:
(a) , where
(b) T(P1)=1, where T(P1) =no. of 0-1 transitions of
(c)
(d)
P9
P2
P3
P8
P1
P4
P7
P6
P5
N(P1)=P2+P3+...+P8+P9
Figure 13.8
Neighborhood
arrangement used by the thinning algorithm

## Slide 40: Skeletons
,
Step2: flags for deletion, if
(a)remains the same , where
(b)remains the same T(P1)=1, where T(P1) is the no. of 0-1 transitions of
(c)
(d)
Figure13.9
illustrations of conditions (a) and (b) in equation on page 11. In this case N( and T(
0
0
1
1
P1
0
1
0
1
ee |  | 

## Slide 41: Skeletons
Step 1 applied to every border pixel in the binary region under consideration.
If one or more of conditions (a)-(d) are violated, the value of the point is not changed, if all conditions are satisfied, the point is flagged for deletion.
However, the point is not deleted until all border points have been processed.
After step 1 has been applied to all border points, those flagged points are deleted.
Then step 2 applied to the resulting data in exactly the same manner as step 1.

## Slide 42: Skeletons
Thus one iteration of the thinning algorithm consists of:
Applying step 1 to flag border points for deletion;
Deleting the flagged points;
Applying step 2 to flag the remaining border points for deletion;
Deleting the flagged points;
This basic procedure is applied iteratively until no further points are deleted.

## Slide 43: Skeletons
0 | 1 | 0
0 | p | 0
0 | 0 | 0
1 | 1 | 1
1 | p | 1
1 | 0 | 1
1 | 1 | 1
1 | p | 1
1 | 1 | 1
1 | 1 | 0
1 | p | 0
0 | 0 | 0
0 | 0 | 0
0 | p | 1
0 | 1 | 1
N(p1)=1
N(p1)=7
N(p1)=8
p4 or p6=0
p2 or p8=0
0 | 0 | 0
1 | p | 1
0 | 0 | 0
T(p1)=2

## Slide 44: Skeletons

## Slide 45: Boundary Fitting
Curve fitting: given a point set (xi, yi)，find out a function f (x), and let the MSE (Mean square error) of below expression is the smallest:
N is the point number
If we assume f(x) is a Parabolic Curve, it expression is:

## Slide 46: Boundary Fitting
Curve fitting is the process to ensure optimal parameter. It can be solved by classic least square method. Let:
Error vector:
E=Y－BC
Notes: B的最左一列应该为1？

## Slide 47: Boundary Fitting
Mean square error:
Optimal solution is:
Matrix [BBT］-1BT is called the pseudo inverse matrix of B (伪逆矩阵).
We can easily spread it to other coefficient form, such as Circle, Ellipse, Two order quadratic equation, Three order quadratic equation, …
Matlab toolbox is very powerful to do this kind of work.

## Slide 48: Boundary Fitting
Fitting result

## Slide 49: Boundary Descriptors
Position
Direction
Major axis
Length of boundary
Enclose Area
Curvature
Notes: curvature
n. 弯曲，[数] 曲率

## Slide 50: Position
Center of Mass:

## Slide 51: Direction
It is difficult to define the direction of the object. If the object is thin and long, then we can define the direction of long axis is the direction of the object.
D is a distance measure
pi and pj are points on the boundary B
Also called Major axis.

## Slide 52: Major Axis
Ratio of the major to the minor axis.
Major axis = the line connecting the two extreme points that comprise the diameter.
Minor axis = the line perpendicular to the major axis.
A
B

## Slide 53: Length of a Boundary
Ne: the number of even in the chain code.
No: the number of odd in the chain code.
The number of pixels along a boundary.
C(i+1,j+1)
D(i+1,j)
4 directional chain code:
8 directional chain code:

## Slide 54: Enclose Area
(1)Feret box (外接盒): defined direction
(2)minimum enclosing rectangle，MER (最小外接矩形): arbitratry direction
(3) Convex hull (凸包)

## Slide 55: Minimum Enclosing Rectangle
Rectangle
Minimum Enclosing Rectangle
x
y
x
y
O
(
a
)
(
b
)
O

## Slide 56: Minimum Enclosing Rectangle
AO is the area of the object, AMER is the area of MER (最小外接矩形). The value of R is in [0, 1], When the object is a rectangle, R=1.0, for a circle, R=π/4, for a triangle R=0.5, and for thin-long object, R will be smaller.
WMER and LMER are the width and length of MER, we can use r to distinguish thin-long object from circle or rectangle object.
Rectangle degree:
Notes: eccentricity
n. 古怪；怪癖；[数] 离心率

## Slide 57: Curvature
The rate of change of slope
Difficult to do as digital boundaries tend to be locally “ragged”
Using the difference between the slopes of adjacent boundary segments (which represented as straight lines)
E.g.: k1, and k2 are the slopes of two neighbor lines, and then the curvature at point a is k1-k2.

## Slide 58: Curvature
As the boundary if traversed in the clockwise direction, a vertex point p is said to be the part of convex if the change in slope at p is nonnegative. Otherwise, p is said to belong to a concave.
Line (if the change is less than 10 degrees) and corner (changes exceeds 90 degrees)
Curvature of P1>0: Convex
Curvature of P2<0: Concave
Notes: concave
adj. 凹的，凹面的; n. 凹面; v. 使变凹形

## Slide 59: Summary
We have looked at:
  Overview
  Representation
  Boundary descriptor